## Slide 1
DEPTH-SENSE HELMET
Prosthesis Vision Assistance for Visually
2023-2024
PAOLO MAGRI
MATTIA SAPUTO
LORENZO TURLA

## Slide 2
01
Connection via USB port to the computer placed in the backpack
02
03
OVERVIEW
Helmet equipped with a camera featuring depth sensor and object detection
Connected with ear-pods featuring transparency mode to not limit listening

## Slide 3
PROGRESS
OUR SOLUTION
FUTURE SOLUTION
OLD SOLUTION
Limited Distances
Touch needed
Hands-Free
Object Recognition
New tasks
Greater Comfort

## Slide 4
CAMERA
OAK-D PRO
IR illumination LED enables running AI and CV algorithms in low-light or no-light environments
NIGHT VISION
Depht perception for low visual intrest surface by projecting thousands of IR dots to the scene
DEPTH
12MP central RGB camera auto-focus and fixed-focus variants
RGB

## Slide 5
AIR-PODS PRO
TRASPARENCY MODE
User could be aware if the obstacle is at left or at right and secondly
AUDIO PANNING
Listen feedback sounds at the same time to be careful of the environment

## Slide 6
ALGORITHMS
YOLO v4
realtime object detection
STEREO CAMERA
sensor fusion
DEPTH ANALYSIS
OBJECT DETECTION

## Slide 7
DEPTH ANALYZER
Three different sound frequencies based on the distance of the object
3m - 2m - 1m
Distance plot for recalibration according to personal preferences
Stereo fusion between two monocular depth cameras
Wide visual range of up to 10 meters

## Slide 8
OBJECT DETECTION
YOLO v4
Expandable and customizable dataset for object and human recognition
Automatic creation of different ROIs and nearest one priority

## Slide 9
USER TRAINING
Dynamic Phase:
Moving Subject Recognizing Distances and Getting Accustomed to Sound Frequency Differences
Initial Phase:
Object and Shape Recognition in Static Positions
TWO-PHASES
01
02

## Slide 10
FUTURE IMPLEMENTATIONS
Controller for tasks, zoom, contrast, and also lighting in low-light conditions
03
Implementation of an Arduino board with battery
02
Algorithm reading implementation
01

## Slide 11
Limitations in acquisition quality due to camera resolution and algorithms
Difficulty in recognizing objects not present in the dataset
The computational power of the computer that slows down real-time acquisition
PROBLEMS

## Slide 12
2023-2024
THANK YOU
PAOLO MAGRI
MATTIA SAPUTO
LORENZO TURLA
CONTACT US FOR MORE DETAILS
p.magri005@studenti.unibs.it
m.saputo001@studenti.unibs.it
l.turla002@studenti.unibs.it